## Slide 1
DIGITAL DESIGN · COMPUTER ARCHITECTURE
4-Bit
Ripple Carry
Adder
Digital Design and Computer Architecture
SECTION - 4
01 / 07
PRESENTED BY :
VIJAY -2620030270
SAI VIKRANTH -2620030268
GAYATHRI - 2620030290
AKSHAYA -2620030308
Notes: Introduce the 4-bit ripple carry adder as a compact example of how simple logic blocks become a multi-bit arithmetic circuit.

## Slide 2
LECTURE · 01
4-Bit Ripple Carry Adder
ORIENTATION
Binary arithmetic
Introduction and Objective
1
Introduction
A 4-bit ripple carry adder (RCA) adds two 4-bit binary numbers using four cascaded full adders.
2
Purpose
Design and verify the 4-bit RCA in Logisim, and explain how the carry ripples from bit 0 to bit 3.
3
Scope
Full-adder theory, the Logisim implementation, simulation results, and applications with limitations.
02 / 07
Notes: Frame the session around one circuit and four questions: what a full adder does, how four stages connect, how to verify the outputs, and why carry delay matters.

## Slide 4
03 · THEORY
4-Bit Ripple Carry Adder
THEORY
Logic and circuit
Theory and logic circuit
Full adder: adds bits A, B, and carry-in Cin, producing Sum and carry-out Cout.
Sum = A ⊕ B ⊕ Cin Cout = AB + BCin + ACin
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
4-bit RCA circuit: FA0 → FA1 → FA2 → FA3, with C0 = 0; each carry C1, C2, C3 feeds the next stage and C4 is the final carry.
03 / 07

## Slide 5
04 · LOGISIM
4-Bit Ripple Carry Adder
IMPLEMENTATION
Four-stage design
Circuit design in Logisim
Four full-adder stages are wired in cascade; each stage adds one bit pair plus the carry from the previous stage.
FA0
A0, B0, C0 = 0
→ S0, C1
FA1
A1, B1, C1
→ S1, C2
FA2
A2, B2, C2
→ S2, C3
FA3
A3, B3, C3
→ S3, C4
Working: addition starts at the least significant stage; each carry must settle before the next stage gives its final sum and the final carry C4.
[PLACEHOLDER: insert your Logisim screenshot of the 4-bit RCA circuit here]
04 / 07

## Slide 7
05 · SIMULATION
4-Bit Ripple Carry Adder
RESULTS
Inputs and outputs
Simulation results
Full-adder truth table: each input row yields Sum and Cout.
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
[PLACEHOLDER: Logisim screenshot of simulation output for the 4-bit adder]
[PLACEHOLDER: input-output combinations observed in Logisim]
[PLACEHOLDER: observed S3-S0 and C4 values from your run]
05 / 07

## Slide 8
06 · CONCLUSION
4-Bit Ripple Carry Adder
WRAP-UP
Applications and next steps
Conclusion and applications
Outcome: four cascaded full adders form a working 4-bit RCA.
Advantages: simple design and low complexity.
Limitation: carry delay grows as bit width increases.
Applications: ALUs, processor datapaths, calculators, embedded arithmetic.
Improvements: carry-lookahead, carry-select, or carry-skip adders for faster carry.
GitHub repository / project files: [PLACEHOLDER: insert GitHub repository link]
06 / 07

## Slide 9
Geo Tag Photo

## Slide 10
Thank You
07 / 07